## Slide 1: Composable Extensions (CX) Task Group Proposal Draft 2024-02-15
Jan Gray, Guy Lemieux Soft CPU SIG
Notes: 1 Welcome to the Composable Extensions Task Group Proposal, from the Soft Processor SIG

## Slide 2: Outline
TG ask, value proposition, support, charter
How it might work from software
Overview of deliverables
Q & A
Notes: Here’s a brief outline
We’ll introduce the task group ask, the value proposition and support for this work, and the draft charter.
How it might work from a software perspective
We’ll introduce both ISA and non-ISA deliverables.
We’ll look at possible CX ISA extensions in more detail
Then take some Q&A

## Slide 3: Composable Extensions TG Value Proposition
We propose a new Task Group
To specify ISA extensions + software and hardware interop interfaces
To compose my composable custom extensions with yours, without prior coordination and without changing our libraries or OS
Enables robust reuse of anyone’s extensions and libraries
Provides uniform software access to such extensions
For a marketplace of extensions & libraries (especially on FPGAs)
↑ uniformity ↑ reuse ↑ agility ↓ conflicts ↓ silos ↓ fragmentation
Notes: There are dozens of custom extensions, proprietary and non-proprietary, but as the custom extension space is unmanaged, without standards or uniformity, there is next to zero reuse of useful custom extensions across organizations.
We aim to fix this.
We propose new task group
To specify ISA extensions, plus uniform software and hardware interoperation interfaces,
To make it easy and routine to compose my composable custom extensions with yours and with others, without prior coordination and without recompiling our libraries or our operating system.
In all this enables robust reuse of anyone’s extension and libraries,
Provides a uniform software programming model access to such extensions
Enabling a marketplace of reusable extensions, libraries, and hardware modules.
This is especially useful on FPGAs, where you will be able to mix and match all these third party extensions and libraries and build a new customized SoC in an hour.
Greater uniformity will improve reuse and reduce siloing and fragmentation.

## Slide 4: Composing Custom Extensions
Accelerated Application (Composed Software)
Accelerated System (Composed Hardware)
CPU0 <2>
CPU1 <2>
Switch
MPEG CXU <4>
MXFP6 CXU <4>
P4 CXU<4>
MXFP6 library
P4 library
Runtime
System CXU map
CPU Metadata
Switch Metadata
MPEG CXU Metadata
CPU RTL
Switch RTL
MPEG CXU RTL
MXFP6 CXU Metadata
P4 CXU Metadata
MXFP6 CXU RTL
P4 CXU RTL
System manifest
Composer
MPEG library
Notes: Here is an example to help illustrate this.
We believe it can be easy and routine to assemble a system mixing reusable packages of composable extensions hardware, and their software libraries, into an accelerated system, running an accelerated application.
Here the application reuses extension software libraries that discover MPEG, MXFP6, and P4 extensions, and issue their respective custom instructions, without conflict.

## Slide 5: Composable Extensions TG Charter https://github.com/riscv-admin/sig-soft-cpu/blob/main/TG/CX/CHARTER.md
Executive Summary
This Charter governs the TG for a Composable Extensions (CX) framework enabling robust composition of multiple independently authored composable custom extensions, alongside legacy custom extensions, assembled conflict-free in one RISC-V system.
By multiplexing the custom opcode space, and adopting common software and hardware interop interfaces, CX enables uniform extension naming, discovery, and versioning, error handling, state context management, extension hardware reuse, and stable software binaries for each target system -- all without a central management authority.
Notes: Here’s the executive summary of the proposed task group.
The primary objective is routine robust composition of any number of so-called composable custom extensions, coexisting with the CPU’s existing custom extensions.
This requires a way to resolve custom opcode collisions, and as well as uniform means for software extension libraries to discover, use, and manage extensions.
All without requiring a central management authority.
After this presentation we invite you to review and comment upon the task group charter on the URL above, which details the current custom extension reuse problem, the TG’s objectives and requirements, deliverables, acceptance criteria, exclusions, collaborations, and history.

## Slide 6: Support for the Task Group
Meta (RISC-V Summit NA 2023)
CX TG supporters/participants
AMD (Xilinx)
Lattice
Bluespec
Antmicro
Alibaba
Individual members
More to come
Notes: Here is some recent support for this work.
At the 2023 North American RISC-V Summit, Meta’s keynote called for standard ways to specify custom extensions and to unify how they are introduced to software.
We believe the interfaces and abstractions we propose and will refine in the task group advance important aspects of this vision.
On the right are some companies that will participate in the CX TG.
Please add your voice of support for this new TG.
Thank you.

## Slide 7: Composable Extension Multiplexing For conflict-free reuse of the custom opcode space
Multiplexing off: legacy custom instructions, unchanged
Extension library:
  Discover: is named extension available here?  CX selector index
  Select: csrrw prev-index,cx_index,index
  Issue: custom-* instructions
CPU:
  Decode: custom-* instruction  (function-ID, operands)
  Issue: send request (state-ID, function-ID, [insn,] operands) to selected extension
  Retire: receive response, update dest-register and cx_status CSR
Notes: The lynchpin of our proposal is a new extension to multiplex the custom opcode space, enabling unlimited conflict-free reuse of these opcodes.
Here’s one way that it might work, as explained in our draft spec.
On power on reset, and whenever multiplexing is turned off, legacy custom instructions operate as before, unchanged.
Later, an extension software library will discover if an extension is available, the select it, prior to issuing its custom instructions.
Discovery is performed in a CX runtime or CX aware operating system, mapping a globally unique standard CX ID into a system and hart specific CX selector index.
Writing this index into a hart’s cx_index CSR enables extension multiplexing and selects the hart’s current composable extension and the extension’s current state context. <>
Then in the CPU hardware,
IN response to a custom opcode, the CPU partially decodes the instruction, fetches operands,
And sends an extension request with the current state ID, function ID, instruction, and operands, to the selected extension.
The extension performs the function and/or redecodes the raw instruction to address extension scoped registers and RAM, possibly updates this state,
And the CPU uses the extension’s response to update a destination register and the cx_status CSR.

## Slide 8: Stateful Composable Extensions
CX custom instructions may be stateful
  May access accumulators, registers, register files, …
  Some CX state accessible as CX scoped CSRs (CX-CSRs)
Uniform CX state context management
  Supports 100s of CX state contexts, per CX, per system
  Any mapping from harts to CX state contexts, 1:1, 1:n, n:1
  The same OS code can save/restore any state context of any CX
Notes: 1 CX custom instructions may be stateful.
2 They may use CX private accumulators, registers, and register files.
3 They may also use CX scoped CSRs, conflict free, uniformly accessed with the usual CSR read/write instructions.
4 There should also be uniform means of selecting and managing CX state contexts.
5 Extension multiplexing supports up to hundreds of state contexts, per extension, per system,
6 And any dynamic mapping from harts to contexts,
7 Although one context per extension per hart will be common.
8 Also, every stateful composable extension includes standard CX-Context CX-CSRs,
9 that provide uniform access to context status and state,
10 So that the same unmodified OS code can manage and context switch any extension state context that is configured in a system.

## Slide 9: Example CX Programming Model, in C++
Notes: 1. This code snippet illustrates a possible programming model for composable extensions,
2. In which an extension library discovers whether the MyEncoder extension is available and selects it.
3. Then for each pair of 8-element vectors,
4. The encoder issues a custom SIMD sum of absolute differences instruction.
5. If the extension is not available the library uses a pure software implementation.
6. For correct composition of libraries, this code obeys a CX-ABI that specifies a callee save discipline for managing the CX multiplexing CSR.
7. Here in lieu of compiler support, we use a C++ object to represent the CX selection scope; when the function returns, the destructor automatically restores the caller’s CX selection..

## Slide 10: Design Tenets
Routine robust reuse of composable extensions & libraries
No prior coordination or central authority
Stable software binaries
Stable modular hardware
Uniform SW: naming, discovery, versioning, state, errors, …
Simple, frugal, fast
Secure
Interop across the decades
Notes: Here are the design tents found in our charter.
1 First, Composition is paramount.
2 It has to be easy robust routine even boring to add a composable extension and libraries to your system even if separately authored across organizations, decades, different platforms and tools.
3 Composition must work without prior coordination or any central naming or numbering authority.
4 Extension libraries must just work, without requiring recompilation or relinking, in a system built with various different organizations’ composable extensions and libraries.
5 Similarly we want to enable module hardware implementations of extensions that just snap into extensible processors without changing for example their instruction decoders.
6 To reduce fragmentation, we require interfaces that afford uniform extension naming, discovery, versioning, state context management, error signaling,
7 The design should be simple, frugal, and fast. And if possible, itself expressed as custom extensions to have no impact on the other standard extensions.
8 It must have a threat assessment, must not introduce side channel attacks, and must provide a means for OS to perform access control to extensions and state.
8 Finally interop interfaces and things they itnterop, tend to last forever, so we require provisions for backwards and forwards compatible versioning of our interfaces and of composable extensions built with them.

## Slide 11: CX TG Extensions and Interface Spec Deliverables
New ISA extension(s): new custom CSRs & multiplexed custom instructions only
New interfaces
  Software: CX-API: extension services: uniform discovery, versioning, state mgmt
  Software: CX-ABI: software rules for CX-Mux CSRs
  Hardware: CXU-LI (logic interface): auto-composition of CPUs + CX Units
 | Unpriv and Priv ISA
CX Multiplexing | mcx_selector cx_status (basic muxing) + mcx_table cx_index (optional privileged access control)
CX State Management | CX scoped custom CSRs + + 3 CX CSRs for OS to read/write any CX state context
11
Notes: 1 This slide summarizes the proposed TG deliverables: ISA extensions and new software and hardware interfaces
2 The new ISA extensions are entirely contained within the custom instructions opcode space and custom CSRs ranges.
3. They provide extension multiplexing and unform extension state context management
3 Both have unpriv and priv ISA aspects..
3 Four new CSRs together provide access controlled composable extension multiplexing, for conflict free custom-* opcodes and conflict-free CX-scoped CSRs
4 Then 3 more CX CSRs enable an OS to uniformly save or restore any CX state context.
4 In summary, we propose zero new instructions, only new custom CSRs and their effects.
5 Then New software interfaces provide uniform CX runtime services including naming, discovery, and versioning, as well as disciplined use of the CX mux CSRs.
6 And a new, optional CXU logic interface enables glueless automatic composition of extensible CPUs and CXs hardware into processor complexes. Again, this is perfect for soft processors.
7 While there are quite a few moving parts, we believe this is a minimum viable set of interop standards to address the soft processor SIG’s extension composition requirements.
8 Given the priv CSRs and OS interactions, we propose the TG be homed in the priv ISA TC.

## Slide 12: Composable Extensions Collateral
TG Charter: https://github.com/riscv-admin/sig-soft-cpu/blob/main/TG/CX/CHARTER.md
Draft Spec: https://raw.githubusercontent.com/grayresearch/CX/main/spec/spec.pdf
Design and Rationale Talk: https://www.youtube.com/watch?v=7daY_E2itpo
Talk slides: https://raw.githubusercontent.com/grayresearch/CFU/main/collateral/design-rationale-CX-CXU-spec.pdf
Repo: https://github.com/grayresearch/CX
Notes: 1 At the formation of the TG we submit the following collateral prepared by the SIG over several years of design iterations.
2 The Task Group Charter
3 A draft proposed specification of the extensions and interfaces, including copious introductory material and rationale.
4 A recording of a design and rationale talk introducing the proposed spec
5 A repository work-in-progress including the spec and implementations of various compsable extension unit hardware modules.

## Slide 13: Task Group Personnel
Past contributors
  Tim Ansell, Tim Callahan, Jan Gray, Karol Gugala, Olof Kingdren, Maciej Kurc, Guy Lemieux, Charles Papon, Tim Vogt (Antmicro, Lattice, Google, Gray Research, QAMCOM, SpinalHDL/VexRiscv, UBC)
TG interest
  AMD, Lattice, Bluespec, AntMicro, Alibaba, individuals
TG Chair/Vice-Chair Interest
  Jan Gray, Guy Lemieux, TBD / open invite
Notes: These original members of the Soft CPU SIG met to work on composable extensions throughout the pandemic years.
Now looking forward we propose to formally undertake CX standardization with RISC-V International as an official task group,
Including the participation of these these individuals and companies.
Jan and Guy, SIG SOFT CPU vice chair and char, are ready to lead the TG but we also have an open call for volunteers

## Slide 14: Conclusion / Q & A
Notes: 1. A Composable Extensions framework will bring a marketplace of reusable custom extensions, libraries, and hardware.
2. This will be especially welcome for the RISC-V soft processor ecosystem. But it is not just for FPGAs.
3. Now in the Winter of Moore’s Law there will be tremendous pressure to add ever more domain specific custom extensions and accelerators in every RISC-V market segment.
4. Standard, uniform Composable Extensions can prevent incompatible extensions silos, and help keep RISC-V simple, agile, and open.
5. Thank you for your attention.
6. We are pleased to take your questions and comments.